## Slide 1: Capability Analysis Table
Capability Analysis Tables are a documentation and paper-equivalent design tool – literally just structured spreadsheets
  Guide conceptual design
  Document each behavior in behavior tree – work at any level of abstraction from component to multi-agent system
Human level tool – not an automated process - pushes designer to clearly describe their desired behavior design, including assumptions and implicit requirements
  Forces designer to consider consistency, behavior structure, and assumptions
    Enables relatively simple checks for sequencing condition violations, exit criteria, and fault management
  Forces designer to consider impact of behavior design on hardware and physical structure and vice versa
    Impact of behavior design on hardware requirements and required capabilities
    Impact of available hardware and existing capabilities on behavior design
Notes: Completely different type of design tool – systems engineering documentation that can represent arbitrary behaviors

## Slide 2: Capability Analysis Table
 |  |  |  | Information Available |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Sample Capability |  |  | None | Internal |  |  |  |  |  |  |  | External |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  | Fixed a priori information |  | Processing Status/Output |  |  |  | Sensors |  |  |  |  |  |  |  | Comms: Mission / Task / Goals |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  | Internal |  | Self/Env |  | External |  | Comms: Non-local sensing |  |  |  |  |  | 
 |  |  |  |  | MAP |  | SELFPOSE |  | LPOSE |  | TEMP |  | TOUCH |  | LIDAR |  | OBJECTPOSE |  |  |  | Sub-Task |  | Notes
 |  |  |  |  | Cond | Beh | Cond | Beh | Cond | Beh | Cond | Beh | Cond | Beh | Cond | Beh | Cond | Beh | Cond | Beh | Cond | Beh | 
Control Mechanisms | Data | Processing | SELFPOSE |  |  |  |  |  |  |  |  |  |  |  |  | BEH1 |  |  | Gen Poses | BEH1 | Ongoing | BEH1 | BEH1 requires LIDAR data and an operator instruction to generate the robot’s position on the map (SELFPOSE) and the relative pose of the nearest object (LPOSE)
 |  |  | LPOSE |  |  |  |  |  |  |  |  |  |  |  |  | BEH1 |  |  | Gen Poses | BEH1 | Ongoing | BEH1 | 
 |  | Movement |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | BEH2 |  |  | Ongoing | BEH2 | BEH2 provides a comms relay service – sensor data from other sources is moved elsewhere
 |  | Storage |  |  |  |  |  |  |  |  |  |  |  | BEH3 |  |  |  |  |  |  | Ongoing | BEH3 | BEH3 logs internal sensor data
 | Hardware | Static H/W |  |  |  |  |  |  |  |  | Temp < T1 | BEH4 |  |  |  |  |  |  |  |  | Ongoing | BEH4 | BEH4 monitors internal temperature . At low temperatures, it controls the heater
 |  | Sensors |  |  |  | BEH5 |  | BEH5 |  |  |  |  |  |  |  |  |  |  |  |  | Ongoing | BEH5 | BEH5 changes the sensor settings based on estimated position in a map
 |  | Actuators |  |  |  |  |  |  |  |  | Temp >= T2 | BEH4 |  |  |  |  |  |  |  |  | Ongoing | BEH4 | BEH4 monitors internal temperature. At high temperatures, It reorients relative to the sun
 |  |  |  |  |  |  |  |  | d(LPOSE) > Thresh2 | BEH6 |  |  |  |  |  |  |  |  |  |  | Subsumes BEH4 | BEH6 | BEH6 generates motion if the distance from the current distance to an object is less than a threshold
 |  |  |  | BEH7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Ongoing; Subsumed by BEH4 and BEH6 | BEH7 | BEH7 is a random walk , always active but subsumed by other behaviors

## Slide 3: Capability Table
Used during design process, before implementation, as part of requirements generation process
  Can also be created after implementation as descriptive documentation and post-design verification support tool
Does not prescribe approach to autonomy design
  Supports analysis at every level of abstraction
  Supports analysis of multi-vehicle behavior design, single vehicle behavior design, component behavior design
Can be used with or without a priori hardware selection
  With:
    Ensures design feasible within context of selected platform
  Without:
    Defines requirements imposed on platform selection process